## Slide 1: Combined test QA: What , why and how?
Notes: What: the process we are looking at (combined screening)
Why: why we need QA
How: a system of QA based on feedback and support

## Slide 2: Why : the effect of errors on the screening program
Notes: So let’s investigate the effects of things that can go wrong in the process.

## Slide 3
Inputs and parameter estimates
Risk
DR/FPR/SPR
Process
Amplification of errors

## Slide 4
Standardisation
MoM values should be centred on 1.0 when viewed together, by gestation, by weight, by smoking status, by ethnicity …
What if this is not true?
Notes: Firstly, let’s look at what can go wrong with the biochemistry. What would happen if the median MoM differed from 1.
Why might this happen?

## Slide 5
Effects of bias – biochemistry
(NT and biochemistry at 12 weeks risk cut-off 1 in 100 at time of test)
A 27% increase in SPR with 70 more ‘positive’ results per 10,000 screening tests than expected.
Notes: The table shows false positive (FPR) and detection rates (DR)
FPR is the proportion of unaffected pregnancies that screen positive
DR is the proportion of affected pregnancies that screen positive
The top row represents the situation where both markers are on target. Other rows show various biases from target.
Take the second row for example, PAPP-A running low so biased towards trisomy 21.
This bias leads to a substantial increase in the SPR.
Note need to update

## Slide 6
Effects of bias - NT
Bias (mm)
FPR
DR
-0.4
1.8%
79%
-0.3
1.9%
80%
-0.2
2.0%
82%
-0.1
2.2%
83%
0
2.6%
85%
0.1
3.1%
86%
0.2
3.7%
87%
0.3
4.6%
88%
0.4
5.7%
90%
Notes: This shows the overall effect of biases from NT.
The effect of a positive bias is to make the detection rate higher (good) but the FPR lower (bad).
The effect of a negative bias is to mate the detection rate lower (bad) but the FPR lower (good).

## Slide 7: Crown rump length

## Slide 8: The (near) perfect world of biochemistry
Median Standard
The median MoM value for any sub-population defined by time period, gestational age, maternal weight, smoking status and ethnicity should lie within 5% of the target value of 1.
Median MoM by gestation
Notes: This is the kind of diagnostic plot we are now getting for the PAPP-A and free β hCG.

## Slide 9
Notes: This is the kind of pattern we see when we plot biochemistry MoM values.
The top graph shows PAPP-A and the bottom one free β hCG.
The data for the second sonographer plotted shows positive biases for PAPP-A and negative biases for free β hCG.
What would these do to the performance of screening?
What about the data for the other two sonographers highlighted?

## Slide 10: Operator effects on biochemistry
There is clear evidence of these effects from many sources
Potential causes include
  case mix
  sample preparation
  storage
  transportation
  CRL measurement
Notes: Here is a list of potential explanations for what we are seeing.
Let’s look at the effect of CRL measurement.
CRL is used to date pregnancies and estimate gestational age.

## Slide 11
Notes: Notice that the biases tend to be in opposite directions.
PAPP-A increases with gestation. Free β decreases with gestational age so in the process of standardisation the effect of an error might be expected to produce biases in opposite directions.
Let’s look into this.

## Slide 12: PAPP-A by gestation
Notes: This is how the median used in the process of producing MoM values varies with gestation.
MoM values are produced by dividing the concentration by this median.

## Slide 13: PAPP-A by gestation

MoM = 1
Notes: Take this value at the middle of week 6.
The concentration is the same as the median so the MoM value is 1.
This sits in the centre of the distribution of unaffected pregnancies.

## Slide 14: PAPP-A by gestation

MoM = 1

MoM = 0.57
Notes: Interpreting the value as if it were measured at 10 weeks produces a MoM value of 0.57.
Now this is close to the middle of the distribution for trisomy 21.
Increasing the gestational age makes the PAPP-A measurement look more like a trisomy 21 measurement.
Decreasing gestational age makes the measurement look more unaffected.

## Slide 15: Free β-hCG by gestation

MoM = 1
MoM =1.2

Notes: This effect happens also with free β hCG.

## Slide 16
Effects of Crown Rump Length (CRL) biases on biochemistry MoM values
(NT and biochemistry at 12 weeks risk cut-off 1 in 100)
Down’s syndrome presents as biochemical immaturity so effects of errors on PAPP-A and free β-hCG combine.
Notes: Here is a summary of the effects starting with biases in CRL.

## Slide 17: How : An effective system of feedback